## Slide 1
CONDENSED VIEWPOINT
01
The problem is simpler than the graph pile made it look.
We are asking what radar measurements do when the spacecraft/object moves along a parabolic path past a target.
NOT THE MAIN QUESTION
Is it water?
That could be a later interpretation, but it is not the first thing this model answers.
MAIN QUESTION
What changes?
Range changes first. Delay, apparent depth, phase, Doppler, and PRF follow from that.
DECK GOAL
Explain the chain
Use fewer graphs and show how to interpret the outputs.
Talk track: one path creates one changing distance, and that changing distance creates the radar effects.

## Slide 2
GEOMETRY
02
One simplified geometry replaces most of the repeated plots.
Condensed interpretation deck; values from local parabolic-motion graph summaries.

## Slide 3
FORMULA CHAIN
03
The interpretation comes from one dependency chain.
PATH
z(x)=z0+a*x^2
The parabola describes how altitude changes near closest approach.
->
RANGE
R=sqrt(x^2+y^2+z^2)
This is the distance from spacecraft/object to the target.
->
RANGE RATE
dR/dt
How quickly the distance changes as it moves.
->
DOPPLER
fD=-2(dR/dt)/lambda
Motion turns range-rate into a frequency shift.
ECHO TIMING
t = 2R/c
Longer range means the echo arrives later.
APPARENT DEPTH
d=(Roff-Rnadir)/n
Extra path can look like vertical depth in the radargram.
PHASE
phase ~ y/R
Side-looking geometry can create nonzero interferometric phase.
Condensed interpretation deck; values from local parabolic-motion graph summaries.

## Slide 4
INTERPRETATION
04
Read the outputs as symptoms of changing range.
Observable
What changes
How to explain it
Range
Gets shortest near closest approach.
This is the source variable; everything else follows from it.
Delay
Later echo when range is longer.
The radar sees distance as time because the pulse has to travel out and back.
Apparent depth
Extra path can appear as depth.
A side path can be drawn as a deeper echo if interpreted as straight down.
Phase
Changes with look direction.
Interferometry can tell whether the echo is straight down or sideways.
Doppler / PRF
Doppler follows dR/dt; PRF must sample it.
PRF is not caused by Doppler, but it must be high enough to avoid aliasing.
Condensed interpretation deck; values from local parabolic-motion graph summaries.

## Slide 5
COMPACT RESULTS
05
The example values are anchors, not the whole story.
APPARENT DEPTH
438.5 m
A 25 km side path can map to about 440 m apparent depth.
EXTRA DELAY
5.21 us
That same path difference is about 5.21 microseconds of extra two-way time.
VHF PHASE
22.5 deg
Side-looking geometry predicts nonzero phase.
MAX DOPPLER
445 Hz
Motion creates a VHF Doppler shift over the aperture.
SIMPLE PRF
890 Hz
A basic no-alias rule says PRF should exceed about twice the max Doppler.
Better interpretation: do not treat each graph as a separate claim. Treat each one as a different measurement of the same geometry.
If the geometry is right, the outputs should agree with each other instead of telling separate stories.
Condensed interpretation deck; values from local parabolic-motion graph summaries.

## Slide 6
WHAT IS MISSING
06
What would make this interpretation stronger?
The parabolic model is useful, but it is still a simplified viewpoint. These are the pieces to check before overclaiming.
GEOMETRY INPUTS
Do we know the real path?
Actual trajectory, altitude at the observation time, ground track, pointing, and target location.
RADAR INPUTS
Do settings support it?
PRF, receive window, pulse compression, antenna pattern, phase calibration, and signal-to-noise.
ENVIRONMENT INPUTS
What else changes range?
Surface topography, ice index, plasma/ionosphere, roughness, and any motion not captured by the simple parabola.
Strongest next step: replace the simple parabola with the real trajectory/geometry, then see whether the same range-based chain still explains the observations.
Talk track: I am not claiming the simplified model is final; I am using it to understand which radar effects should move together.